# Page layout file format:

## General
This document explains the file format used to describe the page layout and the title block of schematic and printed circuits pages.
## Units and coordinates
Sizes and coordinates are given in mm
Coordinates are always relative to a page corner (called the reference corner).
Some items use two coordinates. Each coordinate has its own reference corner
## basic items
Page layout use different basic items:
- Segment (two coordinates)
- Rectangle (two coordinates)
- Text (one coordinate)
- Poly polygon (one coordinate)
Items can be repeated n times, and items having one coordinate can be rotated.
Texts are defined both by the page layout file (fixed text) and by user, at run time (date, title...).
Therefore texts can include format descriptors, which will be replaced by the corresponding string, inside a project.
## Coordinates and reference corners
Each coordinates is relative to a reference corner
The direction of coordinates depends on this reference corner:

## Items options
Item	coordinates	line thickness	Rotation (in degree)	Repeat (X or/and Y)
Line (segment)	2	Yes or default	No	Yes
Rectangle	2	yes or default	No	Yes
Text	1	yes or default	Yes	Yes
Poly polygon	1	Yes (default = 0)	Yes	Yes

## Keywords used in description
page_layout setup left_margin right_margin top_margin bottom_margin linewidth textlinewidth textsize comment line rect polygon tbtext / name	pos start end pts xy maxlen maxheight font bold italic size ltcorner lbcorner rbcorner rtcorner	justify left center right top bottom rotate repeat incrx incry incrlabel

## Comments
Comments are allowed. they are inside (), and start by the keyword comment
Example:
(comment rect around the title block)

## Coordinates
A coordinate is the X pos, the Y pos, and the reference corner (coordinate origin)
the default is the bottom right corner
example:
(start 10 0 ltcorner) or (start 20 10)
The direction depends on the corner: a positive coordinate define a point from the corner origin, to the opposite corner.
## Items
Items are defined by a name, coordinates in mm and some attributes, and can be repeated.
for instance (repeat 2) (incrx 2) (incry 2) repeat the item 2 times, and coordinates are incremented by 2 on X direction, and 2 on Y direction
## Header and setup
( page_layout
(setup (textsize 1.5 1.5) (linewidth 0.15) (textlinewidth 0.15) )
…..

## Line and rect
Lines and rectangles are defined by 2 coordinates start and end, and attributes.
Attributes are linewidth and repeat parameters.
Example:
(line (start 50 2 ltcorner) (end 50 0 ltcorner) (repeat 30) (incrx 50) )
(rect (comment rect around the title block) (linewidth 0.15) (start 110 34) (end 2 2) )

## Texts
### Basic texts
Texts are defined by the text (between quotes), the position, and optional attributes
Example
(tbtext "1" (pos 25 1 lbcorner) (font (size 1.3 1.3)) (repeat 100) (incrx 50) ) (incrlabel 1)
the text can be rotated by (rotation <value>) with value = rot angle in degrees, and the initial text value will be “2” “3” …
### Multi-line texts
Texts can include more than one line.
In files the new line symbol is the 2 chars sequence “\n”, like in C printf format:
'\' followed by 'n'.
Example:
(tbtext "Multi line text\nline 2\nline 3\nline 4" (name text18:Text) (pos 90.3 29))
is the text:
Multi line text
line 2
line 3
line 4
Note also it is possible to insert a “\n” string in the actual text by inserting the “\\\\n” sequence, and a '\' followed by '\' sequence is converted to a single '\' char.
### Font option
Font option is
(font <(size <size X> <size Y>)> <bold> <italic>)

Example
(font (size 1.3 1.3) bold italic) defines a specific size, with both bold and italic options
### Justification
(justify <justif keyword>) controls the text justification (the default is left on X and centered on Y)
justif keywords are center, left, right, top and bottom
(justify center top) is a text centered on X axis and top aligned on vertical axis
If center is used, it should be the first option, because it forces both horizontal and vertical justification to be centered.
### Constrained text
The text size can be constrained:
(maxlen <value>) and (maxheight <value>) force the actual text x and/or y size to be reduced to limit the text height to the maxheight value, and the full text x size to the maxlen value.
If the actual text size is smaller than limits, its size is not modified.
### Format symbols
Texts can include a format symbol, a la printf.
At run time these format symbols will be replaced by their actual value.
Known format symbols are:

%%	replaced by %
%K	Kicad version
%Z	paper format name (A4, USLetter …)
%Y	company name
%D	date
%R	revision
%S	sheet number
%N	number of sheets
%Cx	comment (x = 0 to 9 to identify the comment)
%F	File name
%P	sheet path (sheet full name)
%T	title

Example:
(tbtext \Size: %Z" ...) displays something like "Size A4" or Size USLetter", depending on the selected page format.

## Poly Polygons
Set of filled polygons are supported.
The main purpose is to allow logos, or complex shapes
They support the repeat and rotation options
They are defined by
(polygon (position ..) <rotation> <linewidth> <list of corners>
the parameter linewidth defines the pen size used to draw/plot the polygon outlines (default = 0)
example:
(polygon (pos 134 18 rbcorner) (rotate 20) (linewidth 0.00254)
The list of corners is like
(pts (xy 20.574 8.382) (xy 19.9009 8.382) (xy 19.9009 6.26364) (xy 19.7485 5.98932) .... )

each sequence like
(pts (xy 20.574 8.382) (xy 19.9009 8.382) (xy 19.9009 6.26364) (xy 19.7485 5.98932) .... )
defines a polygon.
Each coordinate is relative to the polygon position.
Therefore a "polygon" is in fact a set of polygons, of a poly polygon

## File format
### Header section
A layout description starts by
( page_layout
and ends by the corresponding closing parenthesis
)
### Setup section
Some default values for parameters can be defined in the setup section:
They are the default text size, the default linewidth, the default textlinewidth and margins.
Example:
( setup (textsize 1.5 1.5) (linewidth 0.15) (textlinewidth 0.15) )
   left_margin 10)(right_margin 10)(top_margin 10)(bottom_margin 10))
If these default values not defined here, Kicad will use internal default values.
### Data section
It contains the list of items (lines, rectangles, texts and poly polygons) to draw.
#### Rect item
Here is a simple example:
    ( rect (comment rect around the title block) (linewidth 0.15) (start 110 34) (end 2 2) )
Here is a more complex example:
    ( rect (start 0 0 ltcorner) (end 0 0 rbcorner) (repeat 2) (incrx 2) (incry 2) )
2 rectangle will be drawn.
The first is drawn from the left top corner of the page, to the right bottom corner
The second is drawn inside the first (from 2 mm of the left top corner of the page, to 2 mm from the right bottom corner of the page)
#### Line item
Here is a simple example:
    ( line (start 110 5.5) end 2 5.5) )
This is a horizontal line near the right bottom corner (default), using the default line thickness.
Here is a more complex example:
    ( line (start 50 2 ltcorner) (end 50 0 ltcorner) (repeat 30) (incrx 50) )
This is a small vertical line (2mm height) at 50 mm of the left top corner, repeated 30 times, on the X axis, every 50mm.
In fact, only segments inside the page will be taken in account.
#### Text item
A text description starts by
 ( tbtext “text to display” (<position>)
and can have attributes:
- font (bold, italic font size)
- rotation
- repeat parameters

Here is a simple text at 109 mm to the left of the right bottom corner and 14.3mm above it:
    ( tbtext "File: %F" (pos 109 14.3) )
This text has a format parameter (%F), which will be replaced by the filename of the sheet at run time, and uses the default size and the default text line width.
It is left justified on the X axis, and center justified on the Y axis (default values)

Here is more complex texts
    ( tbtext "Title: %T" (pos 109 10.7)(font bold (size 2 2)) )
Uses a bold font, with a X size = 2mm, and a Y size = 2mm
    ( tbtext "1" (pos 25 1 ltcorner) (font (size 1.3 1.3))(repeat 100) (incrx 50) )
is a text repeated 100 times (in fact only if items are inside the page)
    ( tbtext "A" (pos 1 25 ltcorner) (font (size 1.3 1.3)) (justify center)(repeat 100) (incry 50) )
Repeated texts have 4 parameters to control duplicate items
repeat	defines the repeat count
incry	defines the step on X axis (default = 0)
incry	defines the step on Y axis (default = 0)
inclabel	define a text modification (default = 1).
his value, if not 0 have meaning only for texts having only one letter.
If this letter is a digit, if will be converted to a number, and each duplicated item will also be a number incremented by inclabel
If this letter is not a digit, each duplicated text will be the letter corresponding to the ascii code incremented by inclabel
( tbtext "1" creates duplicate texts “1”, “2”, … “”9”, “10”, “11” …
( tbtext "A" creates duplicate texts “A”, “B”, …“Z” …

#### Poly polygon item
The poly polygon description starts by (polygon (<position>)
(polygon (pos 134 18 rbcorner)
and can include a rotation, repeat parameters, and linewidth definition.
(rotate 20) (linewidth 0.00254)
Note: the linewidth is used to draw the outlines of the filled polygons.
If not defined, the value 0 is used.
The next info is the list of corners corresponding to filled polygons to draw:
        (pts (xy 8.636 3.4544) (xy 8.62838 3.80238) (xy 8.60298 4.0259) (xy 8.54964 4.17322) ….
       )
defines the 3 first corners of a new polygon.
A corner is decribed by (xy <X pos> <Y pos>), with <X pos> and <Y pos> are coordinates relative to the poly polygon position.

Here is an example of a poly polygon:
    (polygon (pos 134 18 rbcorner) (rotate 20) (linewidth 0.00254)
        (pts (xy 8.636 3.4544) (xy 8.62838 3.80238) (xy 8.60298 4.0259) (xy 8.54964 4.17322)
        (xy 8.45312 4.28752) (xy 8.4455 4.29514) (xy 8.08736 4.52628) (xy 7.66826 4.64058)
        (xy 7.24408 4.62788) (xy 7.05866 4.572) (xy 6.77672 4.37388) (xy 6.5913 4.07924)
        (xy 6.5405 3.74142) (xy 6.54558 3.70078) (xy 6.60146 3.45186) (xy 6.68782 3.25882)
        (xy 6.70052 3.24104) (xy 6.96468 3.03784) (xy 7.35076 2.88798) (xy 7.81812 2.8067)
        (xy 8.0645 2.794) (xy 8.636 2.794) (xy 8.636 3.4544) (xy 8.636 3.4544))
        (pts (xy 17.018 4.04876) (xy 16.7259 4.2291) (xy 16.34744 4.3942) (xy 15.94358 4.46024)
        (xy 15.56766 4.4196) (xy 15.35938 4.3307) (xy 15.13332 4.15544) (xy 14.9733 3.93192)
        (xy 14.86408 3.6322) (xy 14.80058 3.23342) (xy 14.77518 2.70764) (xy 14.77264 2.45364)
        (xy 14.79296 1.77546) (xy 14.859 1.23952) (xy 14.97076 0.82296) (xy 15.1384 0.508)
        (xy 15.33652 0.29718) (xy 15.66418 0.127) (xy 16.06042 0.08382) (xy 16.48714 0.17018)
        (xy 16.68018 0.254) (xy 17.018 0.42672) (xy 17.018 2.23774) (xy 17.018 4.04876)
        (xy 17.018 4.04876))
    )
There are 2 polygons (2 blocks starting by “(pts”)
The set of polygons is rotated by 20 degrees (CCW)
### Example: